## Slide 1: 1. Production Scheduling in Hybrid Flow Shop
The Importance of Production Scheduling
  reduce bottlenecks and downtime
  maintain stock levels
  record and maintain working hours
  optimize workstations and equipment usage
  allocate resources efficiently and optimally
  increase the quality of products
  help keep customer orders fulfilled on time
  ……..
Source from: https://www.smartsheet.com/content/production-scheduling
Notes: Data in different formats, such as numerical data, graphical data, and textual data
With effective processing and analysis, they can provide valuable information to perform a great many significant activities such as decision-making, product design, machine failure detection and others
Each organization has an enormous number of maintenance reports/logs or maintenance work orders that contains maintenance time, equipment or machine, maintenance process, etc., which can help technicians finish a variety of tasks
The considerable quantity of textual information provides new opportunities to explore industrial maintenance approaches

## Slide 2: 1. Production Scheduling in Hybrid Flow Shop
Some special settings in hybrid flow shops (HFS)
  the number of processing stages is at least 2
  each stage has at least one machine in parallel and at least one stage have more than one machines
  all the jobs follow the same workflow (from stage 1 to stage P)
  processing time of the same job differs in different stages
Shen, Y., Zhang, X., & Shi, L. (2022). Joint optimization of production and maintenance for a serial–parallel hybrid two-stage production system. Reliability Engineering & System Safety, 226, 108600.
Notes: Data in different formats, such as numerical data, graphical data, and textual data
With effective processing and analysis, they can provide valuable information to perform a great many significant activities such as decision-making, product design, machine failure detection and others
Each organization has an enormous number of maintenance reports/logs or maintenance work orders that contains maintenance time, equipment or machine, maintenance process, etc., which can help technicians finish a variety of tasks
The considerable quantity of textual information provides new opportunities to explore industrial maintenance approaches

## Slide 3: 2. Current Studies in Hybrid Flow Shop Production Scheduling
Real world scenarios with hybrid flow shops (HFS)
  electronics manufacturing
  paper & textile industries
  production of concrete (precast concrete, modular production)
Classification of hybrid flow shops (HFS)
Ruiz, R., & Vázquez-Rodríguez, J. A. (2010). The hybrid flow shop scheduling problem. European journal of operational research, 205(1), 1-18. (Cited 990)
Layout of the system
Available settings
Objective
Notes: Data in different formats, such as numerical data, graphical data, and textual data
With effective processing and analysis, they can provide valuable information to perform a great many significant activities such as decision-making, product design, machine failure detection and others
Each organization has an enormous number of maintenance reports/logs or maintenance work orders that contains maintenance time, equipment or machine, maintenance process, etc., which can help technicians finish a variety of tasks
The considerable quantity of textual information provides new opportunities to explore industrial maintenance approaches

## Slide 4: 2. Current Studies in Hybrid Flow Shop Production Scheduling
Layout of the HFS ()
  HFI (identical parallel machines): all machines are identical and therefore require the same processing time
  HFU (uniform parallel machines): machines have basically the same characteristics but production speed differs by a given factor (e.g., degradation leads to speed diversities)
  HFR (unrelated parallel machines): machines differ in terms of their properties and have no relation to each other
  DHF (distributed hybrid flow shop): considering different spatially separated factories, and there is an HFS in each factory
Graham, R. L., Lawler, E. L., Lenstra, J. K., & Kan, A. R. (1979). Optimization and approximation in deterministic sequencing and scheduling: a survey. In Annals of discrete mathematics (Vol. 5, pp. 287-326). Elsevier. (Cited 8910)
Example of DHF
Notes: Data in different formats, such as numerical data, graphical data, and textual data
With effective processing and analysis, they can provide valuable information to perform a great many significant activities such as decision-making, product design, machine failure detection and others
Each organization has an enormous number of maintenance reports/logs or maintenance work orders that contains maintenance time, equipment or machine, maintenance process, etc., which can help technicians finish a variety of tasks
The considerable quantity of textual information provides new opportunities to explore industrial maintenance approaches

## Slide 5: 2. Current Studies in Hybrid Flow Shop Production Scheduling
Available settings of the HFS ()
  setup times
  variable speeds
  stochastic influences
  possibility of rejecting certain jobs
Objectives ()
  completion times/makespan (77%)
  punctuality
  environmental sustainability
  monetary
  others
Neufeld, J. S., Schulz, S., & Buscher, U. (2023). A systematic review of multi-objective hybrid flow shop scheduling. European Journal of Operational Research, 309(1), 1-23.
Notes: Data in different formats, such as numerical data, graphical data, and textual data
With effective processing and analysis, they can provide valuable information to perform a great many significant activities such as decision-making, product design, machine failure detection and others
Each organization has an enormous number of maintenance reports/logs or maintenance work orders that contains maintenance time, equipment or machine, maintenance process, etc., which can help technicians finish a variety of tasks
The considerable quantity of textual information provides new opportunities to explore industrial maintenance approaches

## Slide 6: 2. Current Studies in Hybrid Flow Shop Production Scheduling
Some statistics for hybrid flow shop scheduling
Neufeld, J. S., Schulz, S., & Buscher, U. (2023). A systematic review of multi-objective hybrid flow shop scheduling. European Journal of Operational Research, 309(1), 1-23.
Notes: Data in different formats, such as numerical data, graphical data, and textual data
With effective processing and analysis, they can provide valuable information to perform a great many significant activities such as decision-making, product design, machine failure detection and others
Each organization has an enormous number of maintenance reports/logs or maintenance work orders that contains maintenance time, equipment or machine, maintenance process, etc., which can help technicians finish a variety of tasks
The considerable quantity of textual information provides new opportunities to explore industrial maintenance approaches

## Slide 7: 2. Current Studies in Hybrid Flow Shop Production Scheduling
Some statistics for hybrid flow shop scheduling
Neufeld, J. S., Schulz, S., & Buscher, U. (2023). A systematic review of multi-objective hybrid flow shop scheduling. European Journal of Operational Research, 309(1), 1-23.
Notes: Data in different formats, such as numerical data, graphical data, and textual data
With effective processing and analysis, they can provide valuable information to perform a great many significant activities such as decision-making, product design, machine failure detection and others
Each organization has an enormous number of maintenance reports/logs or maintenance work orders that contains maintenance time, equipment or machine, maintenance process, etc., which can help technicians finish a variety of tasks
The considerable quantity of textual information provides new opportunities to explore industrial maintenance approaches

## Slide 8: 3. Model Formulations and Solutions
Four types of MIP formulation
  Sequence-based models: based on predecessor and successor relations
    where the decision is made using binary variable , if job is processed after job
  Position-based formulations: based on the permutation of jobs
    where the decision is made using binary variable , if job is processed at the position
  Time-indexed variables: based on the time-line
    where the decision is made using binary variable , if job is processed at the time unit
  Less considered
  Complexity increase
Neufeld, J. S., Schulz, S., & Buscher, U. (2023). A systematic review of multi-objective hybrid flow shop scheduling. European Journal of Operational Research, 309(1), 1-23.

## Slide 9: 3. Model Formulations and Solutions
Solution representations
  The choice of a solution representation and, thereby, the encoding and decoding of a solution is critical for the performance of a metaheuristic algorithm
Four solution representations methods
  P1: job sequences and machine assignments are defined for each stage explicitly
  P2: all job sequences are defined for each stage individually but the machine assignment follows a given rule
  P3: machine assignment is defined for each stage, while the job sequence is encoded only for the first stage
  P4: only the job sequence in the first stage is encoded.
Fernandez-Viagas, V., Perez-Gonzalez, P., & Framinan, J. M. (2019). Efficiency of the solution representations for the hybrid flow shop scheduling problem with makespan objective. Computers & Operations Research, 109, 77-88.

## Slide 10: 3. Model Formulations and Solutions
Complexity of the four solution representations methods
P1
P2
P3
P4
Fernandez-Viagas, V., Perez-Gonzalez, P., & Framinan, J. M. (2019). Efficiency of the solution representations for the hybrid flow shop scheduling problem with makespan objective. Computers & Operations Research, 109, 77-88.
Completeness or Efficiency ?

## Slide 11: 3. Model Formulations and Solutions
Complexity of the four solution representations methods
Fernandez-Viagas, V., Perez-Gonzalez, P., & Framinan, J. M. (2019). Efficiency of the solution representations for the hybrid flow shop scheduling problem with makespan objective. Computers & Operations Research, 109, 77-88.

## Slide 12: 3. Model Formulations and Solutions
Solutions
Fernandez-Viagas, V., Perez-Gonzalez, P., & Framinan, J. M. (2019). Efficiency of the solution representations for the hybrid flow shop scheduling problem with makespan objective. Computers & Operations Research, 109, 77-88.
  Exact for small-scale problems
  Metaheuristics for general problems

## Slide 13: 4. Reinforcement Learning for HFS Production Scheduling
Reinforcement Learning
  Reinforcement Learning (RL) is a branch of machine learning focused on making decisions to maximize cumulative rewards
  RL has been used for production scheduling as the potential for dynamic scheduling decision making
  RL’s component
    Action space
    State space
    Reward function
    Transition function
  Classification for RL
    Single agent RL (e.g., DQN, DDQN, PPO)
    Multi-agent RL (e.g., QMIX, VDN, MAPPO, or HAPPO)

## Slide 14: 4. Reinforcement Learning for HFS Production Scheduling
Some cases
Zhang, Y., Zhu, H., Tang, D., Zhou, T., & Gui, Y. (2022). Dynamic job shop scheduling based on deep reinforcement learning for multi-agent manufacturing systems. Robotics and Computer-Integrated Manufacturing, 78, 102412.
  Single RL
  Data-drive solution
  Pros
    Real-time scheduling
    Self-learning
  Cons
    Dimension curse of the action and state space
    Output mask

## Slide 15: 4. Reinforcement Learning for HFS Production Scheduling
Some cases
Wang, X., Zhang, L., Lin, T., Zhao, C., Wang, K., & Chen, Z. (2022). Solving job scheduling problems in a resource preemption environment with multi-agent reinforcement learning. Robotics and Computer-Integrated Manufacturing, 77, 102324.
  Multi-agent RL
  Agents can be machines or jobs
  Pros
    Reduce the impact of dimensional curse
    Large-scale problems
    Multi-functional
  Cons
    Additional functional modules to learn inter-agent cooperation
    Poor mobility, compatible from top to bottom

## Slide 16: 5. Project 2 – Case Study
  Hybrid flow shop scheduling in a precast production system
  Aim: Develop production schedules for hybrid flow shops in precast concrete manufacturing by leveraging state-of-the-art algorithms
  Objectives:
    Master the modeling techniques for the precast hybrid flow shop (Problem description)
    Attain expertise in utilizing at least one major optimization solver, e.g., Gurobi or CPLEX (Benchmarks)
    Design and implement a novel meta-heuristic or reinforcement learning algorithm to enhance solution efficiency (Methodology)
  Deliverables: A project report
  Requirements: Introduction, literature review, methodology, and experiments with detailed analysis
  Resources:
    The paradigm of problem description
    Commercial solver usage documentation and tutorials:
      https://www.gurobi.com/documentation/current/refman/py_python_api_overview.html
      https://ibmdecisionoptimization.github.io/tutorials/html/Linear_Programming.html
    Basic code for meta-heuristic and RL algorithms: https://github.com/CI3LAB/CIVIL-6059-Mini-projects-Resources

## Slide 17: 5. Case Study – Solution
Validation – Another algorithm that can deal with the larger problem
  Gantt chart – the final schedule
Small-scale problem

## Slide 18: 5. Case Study – Solution
Validation – Another algorithm that can deal with the larger problem
  Gantt chart – the final schedule
Medium-scale problem

## Slide 19: 5. Case Study – Solution
Validation – Another algorithm that can deal with the larger problem
  Gantt chart – the final schedule
Large-scale problem